## Slide 1: CSCE 5610 Computer System Architecture
The Processor

## Slide 2: Content
Single-cycle implementation
  All operations take the same amount of time—a single cycle.
Multicycle implementation
  Allows faster operations to take less time than slower ones, so overall performance can be increased.
Pipelining
  Lets a processor overlap the execution of several instructions, potentially leading to big performance gains.

## Slide 3: Single-cycle implementation
We will describe the implementation a simple MIPS-based instruction set supporting just the following operations.
Arithmetic: | add | sub | and | or | slt
Data Transfer: | lw | sw |  |  | 
Control: | beq |  |  |  | 
Today we’ll build a single-cycle implementation of this instruction set.
  All instructions will execute in the same amount of time; this will determine the clock cycle time for our performance equations.
  We’ll explain the datapath first, and then make the control unit.

## Slide 4: Computers are state machines
A computer is just a big fancy state machine.
  Registers, memory, hard disks and other storage form the state.
  The processor keeps reading and updating the state, according to the
instructions in some program.
State
CPU

## Slide 5: Instruction fetching
The CPU is always in an infinite loop, fetching instructions from memory and executing them.
The program counter or PC register holds the address of the current instruction.
Read Instruction address [31-0]
Instruction memory
P C
Add
4

## Slide 6: Basic MIPS implementation
The first two steps for every instruction:
Send PC to instruction memory
Read one or two registers using fields in the machine code
Instruction Memory: stores the code and supply instruction given an address
Program Counter (PC): holds the address of the current instruction
Adder: increments the PC to the address of the next instruction

## Slide 7: Building a datapath: Fetch
To execute any instruction:
Fetch the instruction from memory
Increment the PC to point at the next instruction
32-bit Machine Code
PC+4
Why?

## Slide 8
Encoding R-type instructions
Last lecture, we saw encodings of MIPS instructions as 32-bit values.
Register-to-register arithmetic instructions use the R-type format.
  op is the instruction opcode, and func specifies a particular arithmetic
operation.
  rs, rt and rd are source and destination registers.
An example instruction and its encoding:
add $20, $9, $10
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
000000 | 01001 | 01010 | 10100 | 00000 | 1000000

## Slide 9
Registers and ALUs
R-type instructions must access registers and an ALU.
Our register file stores thirty-two 32-bit values.
  Each register specifier is 5 bits long.
  You can read from two registers at a time.
  RegWrite is 1 if a register should be written.
Here’s a simple ALU with five operations, selected by a 3-bit control signal ALUOp.
ALU
ALUOp
Read register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
ALUOp | Function
000 | and
001 | or
010 | add
110 | subtract
111 | slt

## Slide 10
Executing an R-type instruction
Read Instruction
address [31-0]
Instruction memory
Read
register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
Read an instruction from the instruction memory.
The source registers, specified by instruction fields rs and rt, should be
read from the register file.
The ALU performs the desired operation.
Its result is stored in the destination register, which is specified by field rd of the instruction word.
I [25 - 21]
I [20 - 16]
I [15 - 11]
Zero
Result
ALU
ALUOp
op | rs | rt | rd | shamt | func
31 26 | 25 21 | 20 16 | 15 11 | 10 6 | 5 0
RegWrite

## Slide 11: Encoding I-type instructions
The lw, sw and beq instructions all use the I-type encoding.
  rt is the destination for lw, but a source for beq and sw.
  address is a 16-bit signed constant.
Two example instructions:
lw $t0, –4($sp) sw $a0, 16($sp)
op | rs | rt | address
6 bits | 5 bits | 5 bits | 16 bits
100011 | 11101 | 01000 | 1111 1111 1111 1100
101011 | 11101 | 00100 | 0000 0000 0001 0000

## Slide 12: Accessing data memory
For an instruction like lw $t0, –4($sp), the base register $sp is added to the sign-extended constant to get a data memory address.
This means the ALU must accept either a register operand for arithmetic instructions, or a sign-extended immediate operand for lw and sw.
We’ll add a multiplexer, controlled by ALUSrc, to select either a register operand (0) or a constant operand (1).
Write data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Instruction memory
Read Instruction address [31-0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read
register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp
lw $t0, –4($sp)
100011 | 11101 | 01000 | 1111 1111 1111 1100

## Slide 13
MemToReg
The register file’s ― “Write data" input has a similar problem. It must b e able to store either the ALU output of R-type instructions, or the data memory output for lw.
We add a mux, controlled by MemToReg, to select between saving the ALU result (0) or the data memory output (1) to the registers.
Write data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Read Instruction address [31-0]
Instruction memory
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read
register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp

## Slide 14: RegDst
op | rs | rt | address
Write data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
I [25 - 21]
Read Instruction |  | 
address [31-0] |  | 
 |  | I [20 -
Instruction |  | 
memory |  | 
16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read
register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
A final annoyance is the destination register of lw is in rt instead of rd.
lw $rt, address($rs)
We’ll add one more mux, controlled by RegDst, to select the destination register from either instruction field rt (0) or field rd (1).
RegWrite
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp

## Slide 15: Branches
For branch instructions, the constant is not an address but an instruction offset from the current program counter to the desired address.
beq | $at, $0, L | 
add | $v1, $v0, | $0
add | $v1, $v1, | $v1
j | Somewhere | 
L: add | $v1, $v0, | $v0
The target address L is three instructions past the beq, so the encoding of the branch instruction has 0000 0000 0000 0011 for the address field.
Instructions are four bytes long, so the actual memory offset is 12 bytes.
000100 | 00001 | 00000 | 0000 0000 0000 0011
op | rs | rt | address

## Slide 16: The steps in executing a beq
Fetch the instruction, like beq $at, $0, offset, from memory.
Read the source registers, $at and $0, from the register file.
Compare the values by subtracting them in the ALU.
If the subtraction result is 0, the source operands were equal and the PC should be loaded with the target address, PC + 4 + (offset x 4).
Otherwise the branch should not be taken, and the PC should just be incremented to PC + 4 to fetch the next instruction sequentially.

## Slide 17: Branching hardware
We need a second adder, since the ALU is already doing subtraction for the beq.
Multiply constant
by 4 to get offset.
PCSrc=1 branches
to PC+4+(offset 4).
PCSrc=0 continues to PC+4.
4
Shift left 2
PC
Add
Add
0
M
u
x
1
PCSrc
Write data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Read Instruction address [31-0]
Instruction memory
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
Sign
extend
0
M
u x
1
ALUSrc
Zero
Result
ALU
ALUOp

## Slide 18: Control
The control unit is responsible for setting all the control signals so that each instruction is executed properly.
  The control unit’s input is the 32-bit instruction word.
  The outputs are values for the blue control signals in the datapath.
Most of the signals can be generated from the instruction opcode alone, and not the entire 32-bit word.
To illustrate the relevant control signals, we will show the route that is taken through the datapath by R-type, lw, sw and beq instructions.

## Slide 19: R-type instruction path
The R-type instructions include add, sub, and, or, and slt.
The ALUOp is determined by the instruction’s ―"func” field.

## Slide 20: lw instruction path
4
Shift left 2
PC
Add
Add
0
M
u
x
1
PCSrc
Write data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Read Instruction address [31-0]
Instruction
memory
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read register 1
Read
register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp
An example load instruction is lw $t0, –4($sp).
The ALUOp must be 010 (add), to compute the effective address.

## Slide 21: sw instruction path
4
Shift left 2
PC
Add
Add
0
M
u
x
1
PCSrc
Write data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Read Instruction address [31-0]
Instruction
memory
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read register 1
Read
register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp
An example store instruction is sw $a0, 16($sp).
The ALUOp must be 010 (add), again to compute the effective address.

## Slide 22: beq instruction path
The branch may or may not be taken, depending on the ALU’s Zero output
4
Shift left 2
PC
Add
Add
0
M
u
x
1
PCSrc
Write data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Read Instruction address [31-0]
Instruction
memory
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read register 1
Read
register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp
One sample branch instruction is beq $at, $0, offset.
The ALUOp is 110 (subtract), to test for equality.
PCSrc =
0, if branch not-taken
1, if branch taken

## Slide 23: Control Signal Table
Operation | RegDst | RegWrite | ALUSrc | ALUOp | MemWrite | MemRead | MemToReg
add | 1 | 1 | 0 | 010 | 0 | 0 | 0
sub | 1 | 1 | 0 | 110 | 0 | 0 | 0
and | 1 | 1 | 0 | 000 | 0 | 0 | 0
or | 1 | 1 | 0 | 001 | 0 | 0 | 0
slt | 1 | 1 | 0 | 111 | 0 | 0 | 0
lw | 0 | 1 | 1 | 010 | 0 | 1 | 1
sw | X | 0 | 1 | 010 | 1 | 0 | X
beq | X | 0 | 0 | 110 | 0 | 0 | X
sw and beq are the only instructions that do not write any registers.
lw and sw are the only instructions that use the constant field. They also depend on the ALU to compute the effective memory address.
ALUOp for R-type instructions depends on the instructions’ func field.
The PCSrc control signal (not listed) should be set if the instruction is beq
and the ALU’s Zero output is true.

## Slide 24: Generating Control Signals
The control unit needs 13 bits of inputs.
  Six bits make up the instruction’s opcode.
  Six bits come from the instruction’s func field.
  It also needs the Zero output of the ALU.
The control unit generates 10 bits of output, corresponding to the signals mentioned on the previous page.
Read Instruction address [31-0]
Instruction memory
Control
I [31 - 26]
I [5 - 0]
RegDst RegWrite
ALUSrc ALUOp
MemWrite MemRead MemToReg
PCSrc
Zero

## Slide 25: Single-Cycle Performance
We saw a MIPS single-cycle datapath and control unit.
Then, we’ll explore factors that contribute to a processor’s execution time, and specifically at the performance of the single-cycle machine.
Next, we’ll explore how to improve on the single cycle machine’s performance using pipelining.

## Slide 26: Processor clock period
the clock synchronizes the processor’s operations on rising & falling edges:
    a register updates contents upon arrival of clock edge
    a processor starts instruction execution at clock edge
0 Volts
1.2 Volts
Time
Clock Signal
Clock Cycle 1
Clock Cycle 3
Clock Cycle 4
Clock Cycle 2
the processor clock oscillates between high and low signal levels:
Clock Period = Clock Cycle Time
    interval of time between 2 adjacent rising edges
    duration of 1 cycle of the clock signal
    clock period has units of seconds (nanoseconds, microseconds, or picoseconds)
Oscilloscope Operation

## Slide 27: Edge-triggered State Elements
In an instruction like add $t1, $t1, $t2, how do we know $t1 is not updated until after its original value is read?
We’ll assume that our state elements are positive edge triggered, and are updated only on the positive edge of a clock signal.
  The register file and data memory have explicit write control signals, RegWrite and MemWrite. These units can be written to only if the control signal is asserted and there is a positive clock edge.
  In a single-cycle machine the PC is updated on each clock cycle, so we don’t bother to give it an explicit write control signal.
Read register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
Write data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
PC

## Slide 28: Processor Frequency
10 nsec clock cycle period  100 MHz clock rate
5 nsec clock cycle period  200 MHz clock rate
2 nsec clock cycle period  500 MHz clock rate
1 nsec (10-9) clock cycle period  1 GHz (109) clock rate
500 psec clock cycle period  2 GHz clock rate
250 psec clock cycle period  4 GHz clock rate
200 psec clock cycle period  5 GHz clock rate
Clock Frequency = 1 / (Clock Period)
Cycle 1
Cycle 2
Cycle 3
one clock period
When designing processors, we work in units of:
Nanoseconds
or
GHz
    the number of clock cycles occurring in 1 second
    measured in units of Hertz (Hz)
    also called the Clock Rate
a CPU’s Clock Frequency is the inverse of it’s Clock Cycle time
F = 1 / Period

## Slide 29: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count

## Slide 30: CPU Time Exercise
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2× clock cycles
How fast must Computer B clock be?

## Slide 33: CPI-Cycles per Instruction
The average number of clock cycles per instruction, or CPI, is a function of the machine and program.
  The CPI depends on the actual instructions appearing in the program— a floating-point intensive application might have a higher CPI than an integer-based program.
  It also depends on the CPU implementation. For example, a Pentium can execute the same instructions as an older 80486, but faster.
We assumed each instruction took one cycle, so we had CPI = 1.
  The CPI can be >1 due to memory stalls and slow instructions.
  The CPI can be <1 on machines that execute more than 1 instruction per cycle (superscalar).

## Slide 34: CPU Time

## Slide 35: Instructions Executed
Instructions executed:
  We are not interested in the static instruction count, or how many
lines of code are in a program.
  Instead we care about the dynamic instruction count, or how many instructions are actually executed when the program runs.
Ostrich:
li $4,
subi $4,
bne $4,
1000
$4, 1
$0, Ostrich

## Slide 36: Instructions Executed
Instructions executed:
  We are not interested in the static instruction count, or how many
lines of code are in a program.
  Instead we care about the dynamic instruction count, or how many instructions are actually executed when the program runs.
  There are three lines of code below, but the number of instructions executed would be 2001.
Ostrich:
li $4,
subi $4,
bne $4,
1000
$4, 1
$0, Ostrich

## Slide 37: Clock Cycle Time
One "cycle" is the minimum time it takes the CPU to do any work.
  The clock cycle time or clock period is just the length of a cycle.
  The clock rate, or frequency, is the reciprocal of the cycle time.
Generally, a higher frequency is better.
Some examples illustrate some typical frequencies.
  A 500MHz processor has a cycle time of 2ns.
  A 2GHz (2000MHz) CPU has a cycle time of just 0.5ns.

## Slide 38: How does add go through the datapath
4
Shift left 2
PC
Add
Add
0
M
u
x
1
PCSrc
Write data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Read Instruction address [31-0]
Instruction
memory
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read register 1
Read
register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp

## Slide 39: Compute the longest path in the add instruction
I [15 - 11]
Read Instruction
address [31-0]
Instruction memory
Write
data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u x
0
MemToReg
4
Shift left 2
PC
Add
Add
0
M
u
x
1
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
I [25 - 21]
I [20 - 16]
0
M
u
x
1
Read register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
PC+4
2 ns
2 ns
1 ns
RegDst I [15 - 0] 0 ns
0 ns
ALUOp
2 ns
2 ns
2 ns
PCSrc
0 ns
0 ns

## Slide 40: The Slowest Instruction...
If all instructions must complete within one clock cycle, then the cycle time has to be large enough to accommodate the slowest instruction.
For example, lw $t0, –4($sp) is the slowest instruction needing ___ns.
— Assuming the circuit latencies below.
0
M
u x
1
Read Instruction address [31-0]
Instruction memory
Write data
memory
Read Read
address data Write
address
Data
Sign extend
Zero Result
ALU
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
Read register 1
Read
register 2
Write register
Write data
Read data 1
Read data 2
Registers
2 ns
2 ns
2 ns
1 ns
0
M
u x
1
0 ns
1
M
u x
0
0 ns
0 ns
0 ns

## Slide 41: The Slowest Instruction...
If all instructions must complete within one clock cycle, then the cycle time has to be large enough to accommodate the slowest instruction.
For example, lw $t0, –4($sp) is the slowest instruction needing ___ns.
— Assuming the circuit latencies below.
0
M
u x
1
Read Instruction address [31-0]
Instruction memory
Write data
memory
Read Read
address data Write
address
Data
Sign extend
Zero Result
ALU
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
Read register 1
Read
register 2
Write register
Write data
Read data 1
Read data 2
Registers
2 ns
2 ns
2 ns
1 ns
0
M
u x
1
0 ns
1
M
u x
0
0 ns
0 ns
0 ns
8ns
reading the instruction memory 2ns
reading the base register $sp 1ns computing memory address $sp-4 2ns
reading the data memory 2ns
storing data back to $t0 1ns

## Slide 42: ...Determines the Clock Cycle Time
If we make the cycle time 8ns then every instruction will take 8ns, even if they don’t need that much time.
For example, the instruction add $s4, $t1, $t2 really needs just 6ns.
6 ns
reading the instruction memory 2 ns
reading registers $t1 and $t2 1 ns computing $t1 + $t2 2 ns
storing the result into $s0 1 ns
0
M
u x
1
Read Instruction address [31-0]
Instruction memory
Write data
memory
Read Read
address data Write
address
Data
Sign extend
Zero Result
ALU
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
Read register 1
Read register 2
Write
register
Write data
Read data 1
Read data 2
Registers
2 ns
2 ns
2 ns
1 ns
0
M
u x
1
0 ns
1
M
u x
0
0 ns
0 ns
0 ns

## Slide 43: How bad is this?
With these same component delays, a sw instruction would need 7ns, and beq would need just 5ns.
Let’s consider the gcc instruction mix.
Instruction | Frequency
Arithmetic | 48%
Loads | 22%
Stores | 11%
Branches | 19%
With a single-cycle datapath, each instruction would require 8ns.
But if we could execute instructions as fast as possible, the average time per instruction for gcc would be?

## Slide 44: How bad is this?
With these same component delays, a sw instruction would need 7ns, and beq would need just 5ns.
Let’s consider the gcc instruction mix.
Instruction | Frequency
Arithmetic | 48%
Loads | 22%
Stores | 11%
Branches | 19%
With a single-cycle datapath, each instruction would require 8ns.
But if we could execute instructions as fast as possible, the average time per instruction for gcc would be?
(48% x 6ns) + (22% x 8ns) + (11% x 7ns) + (19% x 5ns) = 6.36ns
The single-cycle datapath is about 1.26 times slower!