## Slide 1: CSCE 5610 Computer System Architecture
Instruction Level Parallelism

## Slide 2: Single-Cycle implementation
Why Single-Cycle implementation is not used today?
Requires the same length for every instruction
The clock cycle is determined by the longest possible path (worst case scenario!)
  The load instruction (lw) that uses five functional units in series:
  Inst. Mem  Reg. File  ALU Data Mem.  Reg. File

## Slide 3: A Relevant Question
Assuming you’ve got:
— One washer (takes 30 minutes)
— One drier (takes 40 minutes)
— One “folder” (takes 20 minutes)
It takes 90 minutes to wash, dry, and fold 1 load of laundry.
— How long does 4 loads take?

## Slide 4: The Slow Way
If each load is done sequentially it takes 6 hours
6 PM
Time
30 40 20 30 40 20 30 40 20 30 40 20
7
8
9
10
11
Midnight

## Slide 5: Laundry Pipelining
Start each load as soon as possible
— Overlap loads
Pipelined laundry takes 3.5 hours
6 PM
7 8 9
10
11
Midnight
Time
30 40 40 40 40 20

## Slide 6
Instruction Execution Review
Executing a MIPS instruction can take up to five steps.
However, as we saw, not all instructions need all five steps.
Step | Name | Description
Instruction Fetch | IF | Read an instruction from memory.
Instruction Decode | ID | Read source registers and generate control signals.
Execute | EX | Compute an R-type result or a branch outcome.
Memory | MEM | Read or write the data memory.
Writeback | WB | Store a result in the destination register.
Instruction | Steps required |  |  |  | 
beq | IF | ID | EX |  | 
R-type | IF | ID | EX |  | WB
sw | IF | ID | EX | MEM | 
lw | IF | ID | EX | MEM | WB

## Slide 7
Single-cycle Datapath Diagram
4
Shift left 2
PC
Add
Add
0
M
u
x
1
PCSrc
Write data
memory
Read Read
address data Write
address
Data
MemRead
1
M
u
x
0
MemToReg
Read Instruction address [31-0]
Instruction memory
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read
register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
Sign extend
0
M
u x
1
ALUSrc
ALUOp
2ns
2ns
ALU
Zero
Result
2ns
MemWrite
1ns
RegWrite
How long does it take to execute each instruction?

## Slide 8: Single-cycle Review
All five execution steps occur in one clock cycle.
This means the cycle time must be long enough to accommodate all the
steps of the most complex instruction—a “lw” in our instruction set.
  If the register file has a 1ns latency and the memories and ALU have a 2ns latency, “lw” will require 8ns.
  Thus all instructions will take 8ns to execute.
Each hardware element can only be used once per clock cycle.

## Slide 9: Example: Instruction Fetch (IF)
Read Instruction address [31-0]
Instruction
memory
Write data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
Let’s quickly review how lw is executed in the single-cycle datapath.
We’ll ignore PC incrementing and branching for now.
In the Instruction Fetch (IF) step, we read the instruction memory.

## Slide 10
Instruction Decode (ID)
Read Instruction address [31-0]
Instruction
memory
Write data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
The Instruction Decode (ID) step reads the source registers from the register file.

## Slide 11: Execute (EX)
Read Instruction address [31-0]
Instruction
memory
Write data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
The third step, Execute (EX), computes the effective memory address from the source register and the instruction’s constant field.

## Slide 12: Memory (MEM)
Read Instruction address [31-0]
Instruction
memory
Write data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
The Memory (MEM) step involves reading the data memory, from the address computed by the ALU.

## Slide 13: Writeback (WB)
Write data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp
I [25 - 21]
Read Instruction |  | 
address [31-0] |  | 
 |  | I [20 -
Instruction |  | 
memory |  | 
16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
Finally, in the Writeback (WB) step, the memory value is stored into the destination register.

## Slide 14: A Bunch of Lazy Functional Units
Notice that each execution step uses a different functional unit.
In other words, the main units are idle for most of the 8ns cycle!
  The instruction RAM is used for just 2ns at the start of the cycle.
  Registers are read once in ID (1ns), and written once in WB (1ns).
  The ALU is used for 2ns near the middle of the cycle.
  Reading the data memory only takes 2ns as well.
That’s a lot of hardware sitting around doing nothing.

## Slide 15: Putting Those Slackers to Work
We shouldn’t have to wait for the entire instruction to complete before we can reuse the functional units.
For example, the instruction memory is free in the Instruction Decode step as shown below, so...
Read Instruction address [31-0]
Instruction memory
Write
data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
Instruction Decode (ID)
Idle

## Slide 16: Decoding and Fetching Together
Why don’t we go ahead and fetch the next instruction while we’re decoding the first one?
Write
data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
Read Instruction address [31-0]
Instruction memory
RegWrite
Decode 1st instruction
Fetch 2nd

## Slide 17: Executing, Decoding and Fetching
Similarly, once the first instruction enters its Execute stage, we can go ahead and decode the second instruction.
But now the instruction memory is free again, so we can fetch the third instruction!
Read Instruction address [31-0]
Instruction memory
Write
data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
Decode 2nd
Fetch 3rd Execute 1st

## Slide 18: Break Datapath into 5 Stages
Each stage has its own functional units.
Each stage can execute in 2ns
Read Instruction address [31-0]
Instruction memory
Write
data
memory
Read Read
address data Write
address
Data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign extend
0
M
u x
1
ALUSrc
Zero Result
ALU
ALUOp
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u x
1
RegDst I [15 - 0]
Read register 1
Read register 2
Write register
Write data
Read data 1
Read data 2
Registers
RegWrite
ID
IF
EXE
MEM
WB
2ns
2ns
2ns
2ns

## Slide 19: Pipelining Loads
6 PM
7
8
9
Time
30 40 40 40 40 20
1
2
3
4
Clock cycle 5
6
7
8
9
IF | ID | EX | MEM | WB |  |  |  | 
 | IF | ID | EX | MEM | WB |  |  | 
 |  | IF | ID | EX | MEM | WB |  | 
 |  |  | IF | ID | EX | MEM | WB | 
 |  |  |  | IF | ID | EX | MEM | WB
lw $t0, 4($sp)
lw $t1, 8($sp) lw $t2, 12($sp) lw $t3, 16($sp) lw $t4, 20($sp)

## Slide 20: A Pipeline Diagram
1
2
3
4
Clock cycle 5
6
7
8
9
lw $t0, 4($sp)
sub $v0, $a0, $a1 and $t1, $t2, $t3
or $s0, $s1, $s2 add $sp, $sp, -4
A pipeline diagram shows the execution of a series of instructions.
  The instruction sequence is shown vertically, from top to bottom.
  Clock cycles are shown horizontally, from left to right.
  Each instruction is divided into its component stages. (We show five
stages for every instruction, which will make the control unit easier.)
This clearly indicates the overlapping of instructions. For example, there are three instructions active in the third cycle above.
  The “lw” instruction is in its Execute stage.
  Simultaneously, the “sub” is in its Instruction Decode stage.
  Also, the “and” instruction is just being fetched.
IF | ID | EX | MEM | WB |  |  |  | 
 | IF | ID | EX | MEM | WB |  |  | 
 |  | IF | ID | EX | MEM | WB |  | 
 |  |  | IF | ID | EX | MEM | WB | 
 |  |  |  | IF | ID | EX | MEM | WB

## Slide 21: Pipeline Terminology
1
2
3
4
Clock cycle 5
6
7
8
9
lw $t0, 4($sp)
sub $v0, $a0, $a1 and $t1, $t2, $t3
or $s0, $s1, $s2 add $sp, $sp, -4
filling full emptying
The pipeline depth is the number of stages—in this case, five.
In the first four cycles here, the pipeline is filling, since there are unused
functional units.
In cycle 5, the pipeline is full. Five instructions are being executed simultaneously, so all hardware units are in use.
In cycles 6-9, the pipeline is emptying.
IF | ID | EX | MEM | WB |  |  |  | 
 | IF | ID | EX | MEM | WB |  |  | 
 |  | IF | ID | EX | MEM | WB |  | 
 |  |  | IF | ID | EX | MEM | WB | 
 |  |  |  | IF | ID | EX | MEM | WB

## Slide 22: Pipelining Performance
Compare with other implementations:
  Single Cycle: N cycles or 8N ns for 8ns clock period
How much faster is pipelining for N=1000 ?
1
2
3
4
Clock cycle 5
6
7
8
9
lw $t0, 4($sp)
lw $t1, 8($sp) lw $t2, 12($sp) lw $t3, 16($sp) lw $t4, 20($sp)
IF | ID | EX | MEM | WB |  |  |  | 
 | IF | ID | EX | MEM | WB |  |  | 
 |  | IF | ID | EX | MEM | WB |  | 
 |  |  | IF | ID | EX | MEM | WB | 
 |  |  |  | IF | ID | EX | MEM | WB
filling
Execution time on ideal pipeline:
  time to fill the pipeline + one cycle per instruction
  N instructions -> 4 cycles + N cycles or (2N + 8) ns for 2ns clock period

## Slide 24: Pipelining Other Instruction Types
R-type instructions only require 4 stages: IF, ID, EX, and WB
— We don’t need the MEM stage
What happens if we try to pipeline loads with R-type instructions?
1
2
3
4
Clock cycle
5
6
7
8
9
IF | ID | EX | WB |  |  |  |  | 
 | IF | ID | EX | WB |  |  |  | 
 |  | IF | ID | EX | MEM | WB |  | 
 |  |  | IF | ID | EX | WB |  | 
 |  |  |  | IF | ID | EX | MEM | WB
add $sp, $sp, -4 sub $v0, $a0, $a1 lw $t0, 4($sp)
or $s0, $s1, $s2 lw $t1, 8($sp)

## Slide 27: Important Observation
Each functional unit can only be used once per instruction
Each functional unit must be used at the same stage for all instructions. See the problem if:
  Load uses Register File’s Write Port during its 5th stage
  R-type uses Register File’s Write Port during its 4th stage
1
2
3
4
Clock cycle
5
6
7
8
9
IF | ID | EX | WB |  |  |  |  | 
 | IF | ID | EX | WB |  |  |  | 
 |  | IF | ID | EX | MEM | WB |  | 
 |  |  | IF | ID | EX | WB |  | 
 |  |  |  | IF | ID | EX | MEM | WB
add $sp, $sp, -4 sub $v0, $a0, $a1 lw $t0, 4($sp)
or $s0, $s1, $s2 lw $t1, 8($sp)

## Slide 28: A solution: Insert NOP stages
Enforce uniformity
  Make all instructions take 5 cycles.
  Make them have the same stages, in the same order
    Some stages will do nothing for some instructions
1
2
3
4
Clock cycle
5
6
7
8
9
add $sp, $sp, -4 sub $v0, $a0, $a1 lw $t0, 4($sp)
or $s0, $s1, $s2 lw $t1, 8($sp)
Stores and Branches have NOP stages, too…
IF | ID | EX | NOP | WB |  |  |  | 
 | IF | ID | EX | NOP | WB |  |  | 
 |  | IF | ID | EX | MEM | WB |  | 
 |  |  | IF | ID | EX | NOP | WB | 
 |  |  |  | IF | ID | EX | MEM | WB
R-type | IF | ID | EX | NOP | WB
store | IF | ID | EX | MEM | NOP
branch | IF | ID | EX | NOP | NOP

## Slide 29: Pipeline Registers
We’ll add intermediate registers to our pipelined datapath too.
There’s a lot of information to save, however. We’ll simplify our diagrams by drawing just one big pipeline register between each stage.
The registers are named for the stages they connect.
IF/ID ID/EX EX/MEM MEM/WB
No register is needed after the WB stage, because after WB the instruction is done.

## Slide 30: Pipelined Datapath

## Slide 31: What about Control Signals?
The control signals are generated in the same way as in the single-cycle processor—after an instruction is fetched, the processor decodes it and produces the appropriate control values.
Control signals can be categorized by the pipeline stage that uses them.

## Slide 32: Pipelined Datapath and Control

## Slide 33: Pipelined Datapath and Control

## Slide 34: An Example Execution Sequence
Here’s a sample sequence of instructions to execute.
1000: | lw | $8, | 4($29)
1004: | sub | $2, | $4, $5
1008: | and | $9, | $10, $11
1012: | or | $16, $17, $18 | 
1016: | add | $13, $14, $0 | 
We’ll make some assumptions, just so we can show actual data values.
  Each register contains its number plus 100. For instance, register $8
contains 108, register $29 contains 129, and so forth.
  Every data memory location contains 99.
Our pipeline diagrams will follow some conventions.
  An X indicates values that aren’t important, like the constant field of
an R-type instruction.
  Question marks ??? indicate values we don’t know, usually resulting from instructions coming before and after the ones in our example.
addresses in
decimal

## Slide 35: Cycle 1 (Filling)

## Slide 36: Cycle 2

## Slide 37: Cycle 3

## Slide 38: Cycle 4

## Slide 39: Cycle 5 (Full)

## Slide 40: Cycle 6 (Emptying)

## Slide 41: Cycle 7

## Slide 42: Cycle 8

## Slide 43: Cycle 9

## Slide 44: That’s a lot of Diagrams There
1
2
3
4
Clock cycle 5
6
7
8
9
lw $t0, 4($sp)
sub $v0, $a0, $a1 and $t1, $t2, $t3
or $s0, $s1, $s2 add $t5, $t6, $0
Compare the last nine slides with the pipeline diagram above.
  You can see how instruction executions are overlapped.
  Each functional unit is used by a different instruction in each cycle.
  The pipeline registers save control and data values generated in previous clock cycles for later use.
  When the pipeline is full in clock cycle 5, all of the hardware units are utilized. This is the ideal situation, and what makes pipelined processors so fast.
IF | ID | EX | MEM | WB |  |  |  | 
 | IF | ID | EX | MEM | WB |  |  | 
 |  | IF | ID | EX | MEM | WB |  | 
 |  |  | IF | ID | EX | MEM | WB | 
 |  |  |  | IF | ID | EX | MEM | WB

## Slide 45: Performance Revisited
What is the cycle time of a single-cycle implementation?
  What is its throughput (how many works/instr. finished in a unit of time)?
What is the cycle time of a ideal pipelined implementation?
  What is its steady-state throughput?
How much faster is pipelining?
ALU
Inst mem
Reg Read
Data Mem
Reg Write
Assuming the following functional unit latencies:
3ns 2ns 2ns 3ns
2ns

## Slide 46: Ideal Speedup
1
2
3
4
Clock cycle 5
6
7
8
9
lw $t0, 4($sp)
sub $v0, $a0, $a1 and $t1, $t2, $t3
or $s0, $s1, $s2 add $sp, $sp, -4
In our pipeline, we can execute up to five instructions simultaneously.
  This implies that the maximum speedup is 5 times.
  In general, the ideal speedup equals the pipeline depth.
Why was our speedup on the previous slide ―only "4" times?
  The pipeline stages are imbalanced: a register file and ALU operations can be done in 2ns, but we must stretch that out to 3ns to keep the ID, EX, and WB stages synchronized with IF and MEM.
  Balancing the stages is one of the many hard parts in designing a
pipelined processor.
IF | ID | EX | MEM | WB |  |  |  | 
 | IF | ID | EX | MEM | WB |  |  | 
 |  | IF | ID | EX | MEM | WB |  | 
 |  |  | IF | ID | EX | MEM | WB | 
 |  |  |  | IF | ID | EX | MEM | WB

## Slide 47: The Pipelining Paradox
1
2
3
4
Clock cycle 5
6
7
8
9
lw $t0, 4($sp)
sub $v0, $a0, $a1 and $t1, $t2, $t3
or $s0, $s1, $s2 add $sp, $sp, -4
Pipelining does not improve the execution time of any single instruction. Each instruction here actually takes longer to execute than in a single- cycle datapath (15ns vs. 12ns)!
Instead, pipelining increases the throughput, or the amount of work done per unit time. Here, several instructions are executed together in each clock cycle.
The result is improved execution time for a sequence of instructions, such as an entire program.
IF | ID | EX | MEM | WB |  |  |  | 
 | IF | ID | EX | MEM | WB |  |  | 
 |  | IF | ID | EX | MEM | WB |  | 
 |  |  | IF | ID | EX | MEM | WB | 
 |  |  |  | IF | ID | EX | MEM | WB