## Slide 1: CSCE 5610 Computer System Architecture
Memory Hierarchy

## Slide 2
1) CPU and Memory are located on the motherboard
2) Memory Request Occurs
Instruction: Program Counter contains address of next instruction to fetch
Data: (offset + base) address from lw $t0,offset(base)
3) CPU outputs address bits over Address Bus to Memory and then asserts Control Signals such as R/W and Enable
4) Memory receives address and control, looks up the data value at that address, and sends the data bits over the Data Bus to the CPU
CPU
Memory
address
data
control
Motherboard
COMPUTER ABSTRACTION

## Slide 3
MEMORY HIERARCHY
registers
cache
main memory
(DRAM)
secondary memory
(storage devices: disk, SSD)
tertiary memory
(offline/removable storage: flash, DVD)
~100s psec
~1-10 nsec
~10s nsec
<usec to >msec
varies
speed
increases
< 0.1KB
~10s MB
~10s GB
~10s TB
“infinite”
capacity
increases
“speed” changes 10x per level
capacity changes 1000x per level

## Slide 4: Memory Technology
Static RAM (SRAM)
  $1000 –$2000 per GB
Dynamic RAM (DRAM)
  $5 –$10 per GB
Magnetic disk
  $0.05 –$0.1 per GB
Ideal memory
– Access time of SRAM
– Capacity and cost/GB of disk

## Slide 5
MEMORY HIERARCHY GOAL
Opposing properties of capacity vs speed:
“Large memories are slow.” and “Fast memories are small.”
So how do we create a memory that “gives the illusion” of being large, inexpensive, and fast?
  with hierarchy – leverages locality
    the data at fastest levels is a subset of data at slower levels
  with parallelism – multiple bit access between levels
    word: 32-bits = 4 Bytes transferred at a time (Reg Cache)
    block: 32 to 128 Bytes at a time (Cache Main Memory)
We seek to design hardware such that:
  [ taccess = average access time ] close to registers
  [ $/bit = average cost ] close to secondary storage

## Slide 6
A TYPICAL MEMORY HIERARCHY
Second
Level
Cache
(SRAM)
Control Path
Datapath
Secondary
Memory
(Disk)
Processor Chip
RegFile
Main
Memory
(DRAM)
L1 Instr
Cache
Speed: 1 ~5 ~10 ~50 >10,000
(clock cycles)
Cost: highest high high medium lowest
Memory Hierarchy:
Uses principle of locality to give illusion of memory has the cheapest technology per bit, at the speed offered by the fastest technology
DDR
Module
($/bit)
L1 Data
Cache

## Slide 7
Programs access a small part of address space at any time
  90/10 rule: 90% of time spent in 10% of the total code (loops)
  90% of memory accesses are to 10% of variables in a program
Since memory access is not uniformly distributed during execution and throughout memory range
  Can optimize to make the commonly used data fast:
    Store the 10% commonly used in fast memory
    Store the 90% not frequently used in slow memory
  Results in improved performance vs. cost:
    The system still has fast access time on average
    The system still has low cost per bit on average
90/10 rule:
WHY DOES MEMORY HIERARCHY WORK?
The important property of computer programs used here is locality.

## Slide 8: The Principle of Locality
It’s usually difficult or impossible to figure out what data will be ―most
frequently accessed before a program actually runs, which makes it hard to know what to store into the small, precious cache memory.
But in practice, most programs exhibit locality, which the cache can take advantage of.
  The principle of temporal locality says that if a program accesses one memory address, there is a good chance that it will access the same address again.
  The principle of spatial locality says that if a program accesses one memory address, there is a good chance that it will also access other nearby addresses.

## Slide 9: Temporal Locality in Programs
Loops are excellent examples of temporal locality in programs.
  The loop body will be executed many times.
  The computer will need to access those same few locations of the instruction memory repeatedly.
For example:
— Each instruction will be fetched over and over again, once on every
loop iteration.
Loop: lw | $9, | 0($22)
add | $9, | $9, $10
sw | $9, | 0($22)
addi | $10, | $9, -4

## Slide 10: Temporal Locality in Data
Programs often access the same variables over and over, especially within loops. Below, sum and i are repeatedly read and written.
Commonly-accessed variables can sometimes be kept in registers, but this is not always possible.
  There are a limited number of registers.
  There are situations where the data must be kept in memory, as is the
case with shared or dynamically-allocated memory.
sum = 0;
for (i = 0; i < MAX; i++)
sum = sum + f(i);

## Slide 11: Spatial Locality in Programs
Nearly every program exhibits spatial locality, because instructions are usually executed in sequence—if we execute an instruction at memory location i, then we will probably also execute the next instruction, at memory location i+4.
Code fragments such as loops exhibit both temporal and spatial locality.
sub | $9, | $9, $16
sw | $9, | 0($22)
sw | $9, | 4($22)
sw | $9, | 8($22)

## Slide 12: Spatial Locality in Data
Programs often access data that is stored contiguously.
  Arrays, like a in the code on the top, are stored in memory contiguously.
  The individual fields of a record or object like employee are also kept contiguously in memory.
Can data have both spatial and temporal locality?
employee.name = “Homer Simpson”; employee.boss = “Mr. Burns”; employee.age = 45;
sum = 0;
for (i = 0; i < MAX; i++)
sum = sum + a[i];

## Slide 13
MEMORY HIERARCHY OPERATION
CPU Chip
Main Memory (DRAM chip)
Cache
Block
of 8 words
Line
of 8 words
block containing word in red
being transferred
…
Processor
only referenced word in red
is transferred
1) A word is referenced by Processor via its Byte Address in Main Memory
2) Is that address already in cache?
  YES: access data from cache line
NO: transfer the “containing block” of data from memory to cache
  Line size and Block size are always equal:
  4, 8, 32, … or 128 words
  captures spatial locality
…

## Slide 14: Definitions: Hits and Misses
A cache hit occurs if the cache contains the data that we’re looking for. Hits are good, because the cache can return the data much faster than main memory.
A cache miss occurs if the cache does not contain the requested data. This is bad, since the CPU must then wait for the slower main memory.
There are two basic measurements of cache performance.
  The hit rate is the percentage of memory accesses that are handled
by the cache.
  The miss rate (1 - hit rate) is the percentage of accesses that must be handled by the slower main RAM.
Typical caches have a hit rate of 95% or higher, so in fact most memory accesses will be handled by the cache and will be dramatically faster.
In future lectures, we’ll talk more about cache performance

## Slide 15
THE BASICS OF CACHES
Let’s assume a very simple cache in which the processor requests only one Word and the blocks also consist of one Word.
Cache
Cache
  How do we know if the word referenced is in the cache?
  If it is in cache, how do we find it?

## Slide 16
DIRECT-MAPPED STRATEGY
The simplest way to assign a location in the cache for each word in memory is to assign the cache location based on the address of the word in memory.
  Almost all direct-mapped caches use mod function of address bits to map main memory blocks to their storage location in the cache
  Cache line number for storage =
    { [block address] modulo [number of blocks in the cache] }
mod function can be realized for free by ignoring some higher address bits!!!

## Slide 17
Location determined by address
Direct mapped: only one choice of cache line to use:
  [Block address] mod [#Blocks in cache]
#Blocks is a power of 2
Use low-order address bits to determine bin (cache line)
Here every 8th block of memory maps to same line of cache
DIRECT-MAPPED CACHE
#Blocks in cache = 8
1 mod 8 =1
29 mod 8 =5
Notes: DRAM- 2^5 – 32 bit
Transfer data from low speed to high memory:
They are different position in the cache.
Disadvantage:- Degrad the performace by searching all the cases to find if the a memory needed to be allocatd.
Cache has 8 block
Last 3 bits are used to allocate eht ecache.

## Slide 18
DIRECT-MAPPED CACHE
Since each cache location can contain the contents of different memory locations, how can we know if the data in the cache corresponds to a requested word?
Tag contains the address information to identify whether a word in the cache corresponds to a requested word tag only contains the upper portion of the address corresponding to the bits that are not used as an index into the cache.
Index
Tag
Valid bit indicates whether an entry contains a valid address. If the bit is not set, there cannot be a match for this block For instance, when a processor starts up, the cache does not have good data
Notes: - Tag info used to indentify from which

## Slide 19
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 
DIRECT-MAPPED CACHE: EXAMPLE
Addr (Byte) | Binary addr | Cache line | Hit/Miss
22 | 10 110 |  | 
Given: CPU references addresses {22, 26, 22, 26, 16, 3, 16, 18} in that order.
Sought: Indicate contents of cache after each reference and calculate the hit rate.
Mem[10110] =
data that is stored at address 10110.
reference
information
cache
contents
110
miss
Y
Mem[10110]
10

## Slide 20
DIRECT-MAPPED CACHE: EXAMPLE
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Addr (Byte) | Binary addr | Cache line | Hit/Miss
26 | 11 010 |  | 
reference
information
cache
contents
{22, 26, 22, 26, 16, 3, 16, 18}
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
miss
010

## Slide 21
DIRECT-MAPPED CACHE: EXAMPLE
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Addr (Byte) | Binary addr | Cache line | Hit/Miss
22 | 10 110 |  | 
26 | 11 010 |  | 
reference
information
cache
contents
{22, 26, 22, 26, 16, 3, 16, 18}
110
hit
010
hit

## Slide 22
DIRECT-MAPPED CACHE: EXAMPLE
reference
information
cache
contents
{22, 26, 22, 26, 16, 3, 16, 18}
Addr (Byte) | Binary addr | Cache line | Hit/Miss
16 | 10 000 | 000 | miss
3 | 00 011 | 011 | miss
16 | 10 000 | 000 | hit
?
?
?
?
?
?
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 

## Slide 23
DIRECT-MAPPED CACHE: EXAMPLE
Addr (Byte) | Binary addr | Cache line | Hit/Miss
18 | 10 010 | 010 | miss
For this address reference string {22, 26, 22, 26, 16, 3, 16, 18} on this cache design, a Hit Ratio (or Hit Rate) of (3 hits / 8 references) = 0.375 = 37.5% is obtained.
reference
information
cache
contents
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
?
?
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 

## Slide 24
DIRECT-MAPPED CACHE
Main Memory size is 2a Bytes
given memory is Byte-addressable width of address bus = a bits (for MIPS a=32)
Cache Size is 2n blocks
blocks in cache often referred to as “lines”
If there are 2n lines then n bits are needed to specify the line index
Block size is 2m words:
m bits are needed to specify the word index within block
“main memory block size” is always the same as “cache line size”
Each Word contains 2w Bytes
for MIPS w=2 32-bit word width
Size of tag field:
t bits are needed to uniquely label each item in cache
t = (a – [n+m+w]) bits = (a – n – m – w) bits
because a=t+n+m+w as entire memory address was decomposed into these fields
Let’s calculate the total number of bits in a direct-mapped cache:
Cache
2n lines
2m words
2w Bytes
Main Memory (2a Bytes)
Block
of 2m words
…
…

## Slide 25
DIRECT-MAPPED CACHE
Given:
16MBytes of Byte-addressable main memory
Cache capacity of 64KB = 216 Bytes
Block size is 4 words
Word size is 4 Bytes
How wide is main memory address bus?
2^a = 16MB = (2^4)(2^20) B, thus a=24. Answer: 24 bits
How many blocks are in main memory?
(4 words/block)*(4 Bytes/word)=16 Bytes/block
16MB / (16 Byte/block) = (2^24)/(2^4) blocks = 2^20 blocks. Answer: 1,048,576 blocks
How many lines are in the cache?
Block size in main memory = line size in cache
64KB / (16 Bytes/line) = (2^16)/(2^4) = 2^12 line in cache Answer: 4,096 lines

## Slide 26
DIRECT-MAPPED CACHE
Field Encoding:
  Every address referenced by the processor contains a bits, encoded as:
where
1) Main Memory capacity is 2^a Bytes
2) Cache capacity is…………2^n lines
3) Block/Line size is………….2^m words
4) Each word contains……… 2^w Bytes
5) Tag field width is……………t = (a – n – m – w) bits
t n m w
a
tag line word Byte

## Slide 27
DIRECT-MAPPED CACHE: EXAMPLE
Given: You are tasked to design MIPS-based ultra-lightweight IoT sensor powered only by ambient wifi signals. It has 256 Bytes of main memory, a 64-Byte direct-mapped cache, and block size of 2 words.
Sought: address field encoding.
1) How many bits wide is the address bus?
256=2^a a=8. Answer: 8 bits
2) How many lines are in the cache?
64 Bytes / (4 Byte/word) = 16 words in cache
(16 words)/(2 words/line)=2^3=8 lines n=3 Answer: 8 lines
3) What is the bit field encoding for memory addresses?
MIPS has 32-bit word = 4 Bytes so 2^w=4 w=2.
It is given that 2^m=2 word/block m=1.
So a=8, n=3, m=1, w=2 thus t=8-3-1-2=2 so t=2.
Substituting into:
Field Encoding:
t n m w
a
tag line word Byte
2 3 1 2
tag line word Byte
How are these bits used by the cache?

## Slide 28
DIRECT-MAPPED CACHE
2 3 1 2
tag line word Byte
Line
Index
Fetch a pair of words at a time
because block size = 2 words
(w uses 1 bit so either w=0 or w=1
for word 0 or word 1, respectively )
word 0
word 1
word 0
word 1
Cache
V XY
V XY
tag: one tag field per line covers ALL of the words in that line. In this example, the tag field has 2 bits.
valid: one valid bit per line covers ALL of the words in that line

## Slide 29
Cache
V XY
V XY
Given the cache on the previous slide:
8 lines deep
2 data words per line
Thus, cache capacity = 16 words of data
2-bit tag field per line
1 valid bit per line
32 bits per word
Direct-mapped strategy
Calculate total number of storage bits needed to implement this cache:
(# cache lines) ×[ number of bits required per line ] =
8 × [1+2+32+32] = 8*67 = 536 bits inside
tag
valid
DIRECT-MAPPED CACHE

## Slide 30
Given: A direct-mapped cache containing 64 lines with block size of 16 Bytes (4 words).
Sought: Which line in the cache would hold the content in main memory address 1200?
We can use the bit-field encoding:
64 = 2^n lines in cache n=6
It is given that 2^m=4 word/block m=2
It is given that 16 Bytes are 4 words so 4 Bytes/word = 2^w=4 w=2
Memory address 1200 is the Byte address and written in binary 1200 = 10010110000
So according to the field encoding:
address 1200 gives contents of the line field = 001011two = 11ten it resides in block 11ten
t n m w
a
tag line word Byte
t 6 2 2
… 1 001011 00 00
DIRECT-MAPPED CACHE
Notes: Binary representation

## Slide 31
USE OF SPATIAL LOCALITY
Assume main memory has a total size of 16 words 2a=16 a=4
Assume cache has total size of 4 words and each line holds 2 words
  4/2 = 2 lines 2n = 2 n=1
  Each cache line holds two words 2m=2 m=1
Assume Word size = 1 Byte so 2w=1 w=0 thus t= a-n-m-w = 4-1-1-0 = 2 bits
2 1 1
tag line word

## Slide 32
USE OF SPATIAL LOCALITY
0
Assuming the memory hierarchy described in the previous slides
Memory reference string: bit format is [ (tag1 tag0 tag) (line up/down) (word left/right) ]
  { 0 1 2 3 5 3 4 15 } in decimal
  0000 0001 0010 0011 0101 0011 0100 1111 in binary
1
2
3
5
3
4
15
00 Mem[0] Mem[1]
miss
00 Mem[0] Mem[1]
hit
00 Mem[2] Mem[3]
00 Mem[0] Mem[1]
miss
hit
00 Mem[2] Mem[3]
00 Mem[0] Mem[1]
miss
00 Mem[2] Mem[3]
00 Mem[0] Mem[1]
01
4
5
hit
00 Mem[2] Mem[3]
01 Mem[4] Mem[5]
hit
00 Mem[2] Mem[3]
01 Mem[4] Mem[5]
00 Mem[2] Mem[3]
01 Mem[4] Mem[5]
miss
11
14
15
  8 requests, 4 misses h=4/8=0.5=50% m=1-h=0.5=50%
hit even
though not seen previously… thanks to spatial locality!
hit even
though not seen previously… thanks to spatial locality!

## Slide 33
TYPES OF CACHE MISSES
Compulsory Miss:
  always miss very first access to a block small impact in practice as access a billion per second
  Solution: prefetching a block of data is brought into the cache before it is actually referenced.
Capacity Miss:
  cache cannot contain all blocks accessed by the program
  Solution: increase cache size (may increase access time)
Conflict Miss:
  multiple memory locations mapped to the same cache location
  Solution 1: increase cache size (may increase access time)
  Solution 2: increase associativity (may increase access time)

## Slide 34
DIRECT-MAPPED CACHE: CONFLICT MISS
0
4
0
12
8
4
0
4
miss
miss
miss
miss
miss
miss
miss
miss
00 Mem(0)
00 Mem(0)
01
4
01 Mem(4)
0
00
00 Mem(0)
11
12
10 Mem(8)
01
4
00 Mem(0)
01
4
11 Mem(12)
8
10
01 Mem(4)
0
00
Cache size = 4 words, 4-bit memory address, 1 word per block, 1 Byte per word
Ping-pong effect due to conflict misses:
i.e. two memory locations that map into the same cache line
solve with associativity
  8 requests, 8 misses hit rate = 0
  available but unused
  { 0 4 0 12 8 4 0 4 } in decimal
  0000 0100 0000 1100 1000 0100 0000 0100 in binary

## Slide 35
ASSOCIATIVITY
We seek more flexible block placement:
In a Direct Mapped cache a memory block maps to exactly one cache line only
At the other extreme, could allow a memory block to be mapped to any cache line so-called Fully Associative cache
A compromise is to divide the cache into sets each of which consists of k ways (so-called k-way Set Associative cache)
  Give k choices/chances for each block of memory to place in cache
  Each memory block maps to a unique set (specified by the index field) and can be placed in any “way” of that “set” there are k choices in the cache for each block

## Slide 36
FULLY-ASSOCIATIVE CACHE
  Every address referenced by processor contains a bits, encoded as:
where
1) Main Memory capacity is 2^a Bytes
2) Each word contains……. 2^w Bytes
3) Block size is……………....2^m words
4) Tag field width is…………….t = (a – m – w) bits
t m w
a
tag word Byte
Size of fully associative cache is not part of encoding, because there are no direct addresses to cache lines.
Field Encoding:

## Slide 37
FULLY-ASSOCIATIVE CACHE
Given: MIPS-based tablet system has 4GB Bytes of main memory, a single-level of fully associative-mapped cache, and block size of 32 words.
Sought: What is the bit-field encoding for memory addresses?
Solution:
MIPS has 32-bit word = 4 Bytes so 2^w=4 w=2.
It is given that 2^m=32 word/block m=5.
4GB main memory = (2^2)(2^30)B a=32,
m=5, w=2 thus t=32-5-2=25 so t=25.
Substituting into:
Answer:
t m w
a
tag word Byte
25 5 2
tag word Byte

## Slide 38
0
4
0
12
8
4
0
4
miss
miss
hit
miss
miss
hit
0000 Mem(0)
0000 Mem(0)
Cache size = 4 words, 4-bit memory address, 1 word per block, 1 Byte per word
  8 requests, 4 misses hit rate = 50%
  { 0 4 0 12 8 4 0 4 } in decimal
  0000 0100 0000 1100 1000 0100 0000 0100 in binary
FULLY-ASSOCIATIVE CACHE
tag word Byte
0
0
4
0100 Mem(4)
0000 Mem(0)
0100 Mem(4)
0000 Mem(0)
0100 Mem(4)
1100 Mem(12)
0000 Mem(0)
0100 Mem(4)
1100 Mem(12)
1000 Mem(8)
0000 Mem(0)
0100 Mem(4)
1100 Mem(12)
1000 Mem(8)
hit
hit
0000 Mem(0)
0100 Mem(4)
1100 Mem(12)
1000 Mem(8)
0000 Mem(0)
0100 Mem(4)
1100 Mem(12)
1000 Mem(8)

## Slide 39
K-WAY SET ASSOCIATIVE CACHE
Field Encoding:
  Every address referenced by processor contains a bits, encoded as:
where
1) Main Memory capacity is 2^a Bytes
2) Each word contains……. 2^w Bytes
3) Block size is……………....2^m words
4) The cache contains....……2^s sets
5) Each set contains…………k lines
6) Tag field width is………….t = (a – s – m – w) bits
t s m w
a
tag set word Byte

## Slide 40
SET ASSOCIATIVE CACHE
Given: An embedded 8-bit microcontroller has 16 Bytes of main memory, a 2-way set associative-mapped cache containing 4 lines, and a block size of 1 word.
Sought: Show bit-field encoding for memory addresses.
Solution:
1) 16B =2^4B memory a=4
2) 8-bit word = 1 Byte so 2^w=1 w=0.
3) It is given that 2^m=1 word/block m=0.
4) 2-way k=2 line/set. So, the number of sets = (2^2 lines)/(2 line/set)=2^1 setss=1.
5) So, t=a-s-m-w= 4-1-0-0 t=3.
Substituting into:
Answer:
t s m w
a
tag set word Byte
3 1
tag set
m and w not part of the encoding because they are zero bits wide

## Slide 41
0
4
0
4
miss
miss
hit
hit
000 Mem(0)
000 Mem(0)
Cache size = 4 words with a 2-way set-associative map, 4-bit memory address, 1 word/block, 1 Byte/word
  { 0 4 0 4 0 4 0 4 } in decimal
  0000 0100 0000 0100 0000 0100 0000 0100 in binary
tag set word Byte
0
0
3
010 Mem(4)
000 Mem(0)
010 Mem(4)
000 Mem(0)
010 Mem(4)
SET ASSOCIATIVE CACHE
1
  Set 0
  Set 1
  8 requests, 2 misses … compare to direct-mapped miss rate=8/8
Notes: -

## Slide 42
REPLACEMENT POLICIES
What occurs when Cache is full?
  move blocks to next level of cache but which one?
1) Direct Mapped Caches
  no replacement policy needed
  no alternatives possible because memory address is directly mapped to cache line index
  whenever a miss occurs then line is replaced, no matter how recent thus jeopardizing temporal locality
2) Fully Associative and Set Associative Caches
  need to decide which block to replace (keep ones likely to be used in cache)
  Least Recently Used (LRU): looks backwards in time to predict future accesses
  Least Frequently Used (LFU): counts occurrence of reference without regards to time of reference.

## Slide 43
0
4
0
12
9
4
0
4
miss
miss
hit
miss
miss
miss
000 Mem(0)
000 Mem(0)
Cache size = 4 words with a 2-way set-associative map with LRU replacement policy, 4-bit memory address, 1 word/block, 1 Byte/word
  8 requests, 6 misses hit rate = 25%
  { 0 4 0 12 9 4 0 4 } in decimal
  0000 0100 0000 1100 1001 0100 0000 0100 in binary
tag set word Byte
0
0
3
010 Mem(4)
000 Mem(0)
010 Mem(4)
000 Mem(0)
010 Mem(4)
000 Mem(0)
110 Mem(12)
100 Mem(9)
000 Mem(0)
110 Mem(12)
100 Mem(9)
miss
hit
010 Mem(4)
110 Mem(12)
100 Mem(9)
010 Mem(4)
000 Mem(0)
100 Mem(9)
SET ASSOCIATIVE CACHE WITH LRU
1
  Set 0
  Set 1
  Set 0
  Set 1
110
12
010
4
000
0

## Slide 44
REPLACEMENT POLICIES
  Least Recently Used (LRU) Policy
  Looks backwards in time as some prediction of future accesses
    assumes temporal locality is prevalent
  Hardware Implementation:
    Provide a hardware counter that is incremented with each reference to a cache line
    Example: 4 lines of associativity 2-bit counter
    1) reset counter for line accessed to 0
    2) increment counter of other line
    3) When miss occurs, replace line with highest count

## Slide 45
REPLACEMENT POLICIES
  Least Frequently Used (LFU) Policy
  When capacity miss occurs replace line with fewest references so far in the string
  Hardware Implementation:
    Provide a hardware counter for each line that is only incremented if that cache line is accessed
    When miss occurs, replace the line with the lowest count

## Slide 46
0
0
4
12
9
4
0
4
miss
hit
miss
miss
miss
miss
000 Mem(0)
000 Mem(0)
Cache size = 4 words with a 2-way set-associative map with LFU replacement policy, 4-bit memory address, 1 word/block, 1 Byte/word
  8 requests, 5 misses hit rate = 37.5%
  { 0 0 4 12 9 4 0 4 } in decimal
  0000 0000 0000 1100 1001 0100 0000 0100 in binary
tag set word Byte
0
0
3
000 Mem(0)
010 Mem(4)
000 Mem(0)
010 Mem(4)
000 Mem(0)
110 Mem(12)
100 Mem(9)
000 Mem(0)
110 Mem(12)
100 Mem(9)
hit
hit
000 Mem(0)
010 Mem(4)
100 Mem(9)
000 Mem(0)
010 Mem(4)
100 Mem(9)
SET ASSOCIATIVE CACHE WITH LFU
1
  Set 0
  Set 1
  Set 0
  Set 1
110
12
010
4

## Slide 47
CACHE PERFORMANCE
CPU Time: Clock cycles that the CPU spends executing the program plus the clock cycles that the CPU spends waiting for the memory system.
Memory-Stall Clock Cycles: sum of the stall cycles coming from memory access operations
Memory-Stall Clock Cycles = (Memory Access/Program) × Miss rate × Miss Penalty
CPU Time = (CPU execution clock cycles + Memory-stall clock cycles) × Clock cycle time
Memory-Stall Clock Cycles = (Instructions/Program) × (Misses/Instruction) × Miss Penalty
OR

## Slide 48
CACHE PERFORMANCE: EXAMPLE
Given: Assume a processor with a CPI of 2 is running a program with 36% load and store instructions.
Sought: If the instruction cache and data cache has a miss rate of 2% and 4%, respectively, and the miss penalty is 100 cycles for all misses, determine how much faster a processor would run with a perfect cache that never missed.
Solution:
CPU Time = (CPU execution clock cycles + Memory-stall clock cycles) × Clock cycle time
1) CPU execution clock cycles = Instructions × CPI = 2 × Instructions
2) Memory stall clock cycles = Instruction miss cycles + Data miss cycles
= (Instructions × 0.02 × 100) + (0.36 × Instructions × 0.04 × 100)
= (2 × Instructions) + (1.44 × Instructions) = 3.44 × Instructions
Memory-Stall Clock Cycles = (Instructions/Program) × (Misses/Instruction) × Miss Penalty
4) Speed-up with a Perfect Cache = CPU Time with Stalls/CPU time with perfect caches
= (5.44 Instructions × Clock cycle time ) / (2 × Instructions × Clock cycle time)
= 5.44/2 = 2.72
3) CPU Time = (2 × Instructions + 3.44 × Instructions) × Clock cycle time
= 5.44 × Instructions × Clock cycle time
Notes: CPI = 2, 36% LOAD & STORE INSTRUCTIONS
IF MISS RATE = 0 , IT HIS
MISS RATE:-
INSTRUCTION CACHE = 2%
DATA CACHE – 4%
I X CPI X 2

## Slide 49
CACHE PERFORMANCE: AMAT
Average Memory Access Time (AMAT) metric is used to include the effect of the time to access data for both hits and misses on performance
AMAT= Time for a hit + (Miss rate × Miss Penalty)
AMAT in cache layer n = Miss Penalty in cache layer n-1
AMAT can be calculated based on seconds or # of clocks.

## Slide 50
AMAT: EXAMPLE
Given: Assume a processor with a 1ns clock cycle time, a miss penalty of 20 clock cycles, a miss rate of 0.05 misses per instruction, and a cache access time (including hit detection) of 1 clock cycle.
Sought: Assuming the read and write miss penalties are the same and ignoring other write stalls, find the AMAT for the processor.
Solution:
AMAT= Time for a hit + (Miss rate × Miss Penalty)
1) Time for a hit = cache access time = 1 clock cycles × 1ns clock cycle time = 1ns
2) Miss Penalty = 20 clock cycles × 1ns clock cycle time = 20ns
3) AMAT = 1ns + (0.05 × 20 ns) = 2 ns or 2 clock cycles